# 1. Low-Pass Filter (LPF)
Use when:
- Removing high-frequency noise
- Softening brightness
- Emulating distance / roll-off
- Anti-aliasing before downsampling
Behavior:
Everything below the cutoff passes; above it attenuates.
In EQ practice:
Less commonly used as a “band EQ”; more often used for shaping tone (e.g., warming a mic signal, taming cymbal harshness).

# 2. High-Pass Filter (HPF)
Use when:
- Removing low-frequency rumble, mic-handling noise
- Cleaning up vocals (“rumble-cut”)
- Eliminating sub-bass energy that speakers can’t reproduce
- Tightening mixes by removing mud
Behavior:
Everything above the cutoff passes; below it attenuates.
This is the first filter you insert on almost every live input channel.

# 3. Band-Pass Filter (BPF, “peak-constant gain”)
You are using RBJ’s 2nd BPF form, which has 0 dB gain at center frequency and attenuates above and below.
Use when:
- Isolating a narrow region of interest
- Extracting harmonics
- Emphasizing a resonance without overall gain
- Whistling / tone detection
- Synth design (formants, resonators)
Behavior:
Only a band around f0 passes; the rest is attenuated.
Note:
Not typically used for equalization of full-range audio signals — more a filtering component than a musical EQ.

# 4. Notch Filter (Band-reject)
Use when:
- Removing a specific narrow frequency interference
  - 60 Hz hum + harmonics
  - A feedback whistle
  - A ringing room resonance
- Removing specific spectral components in measurement systems
Behavior:
Everything passes except a narrow band around f0.
Notches are surgical: very high-Q values are common (10–50+).

# 5. All-Pass Filter (APF)
This is one many people skip, but it’s important.
Use when:
- You want to change phase but not magnitude
- Group delay correction
- Phase matching two signals before summing
- Comb-filter cancellation tuning
- Artificial reverb design (all-pass cascades)
Behavior:
Amplitude stays flat, but phase rotates around f0.
In EQ practice:
Rarely used by end users, but heavily used inside reverb/chorus/flanger algorithms.

# 6. Peaking Filter (Bell EQ)
This is the standard EQ band.
Use when:
- Boosting or cutting a specific frequency range
- Correcting room resonances
- Tone shaping (e.g., +3 dB @ 2 kHz on vocals)
- “Fixing harshness,” “adding body,” “cutting mud,” etc.
Behavior:
Boost or cut around f0, size of region determined by Q.
This is 90% of what people think of when they say “parametric EQ band.”

# 7. Low-Shelf Filter
Use when:
- Boosting bass (“add warmth”)
- Cutting bass (“reduce rumble / proximity effect”)
- Shaping overall spectral balance
Behavior:
Frequencies below f0 are boosted or cut.
Above the shelf, response returns toward 0 dB.
Good for musical tone shaping — not surgical.

# 8. High-Shelf Filter
Use when:
- Adding “air,” brightness, sparkle
- Reducing harshness
- General broadband high-frequency shaping
Behavior:
Frequencies above f0 are boosted or cut.
Also very musical; often used on mix busses or mastering EQ.

# 9. “Peak-Constant Gain BPF” vs Peaking EQ
You have two midband filters:
### BPF (0 dB at center frequency)
- Used for filtering, not EQ
- Lets through a narrow slice of spectrum unchanged
- Attenuates outside the band
- No boost at center
### Peaking EQ (boost/cut)
- Used for equalization
- Boosts or cuts around the center
- Returns to 0 dB outside the band
Rule of thumb:
- If you want a “bell-shaped EQ boost,” use peaking.
- If you want “let only 1–3 kHz through,” use BPF.
They look similar mathematically but are used totally differently.

# Summary Table
Filter	Passband	Useful For	Typical Application
LPF	Below cutoff	Remove highs	Noise reduction, tone softening
HPF	Above cutoff	Remove lows	Vocal rumble removal, mix cleanup
BPF	Only near f0	Isolate region	Analysis, detection, synthesis
Notch	Everything except f0	Remove narrow noise	Hum/whistle removal
APF	All frequencies (phase only)	Adjust timing/phase	Reverb, delay design
Peaking (Bell)	Around f0	Boost/cut	Parametric EQ band
Low-Shelf	Below f0	Boost/cut lows	Bass shaping, mastering
High-Shelf	Above f0	Boost/cut highs	Brightness/air shaping
(Your BPF is “constant gain”)	Special variant	Filter-only use	Scientific / algorithmic